## Slide 1: Ladder safety

## Slide 2: Ladders Can take you…
To great heights or on a quick trip to the ground.

## Slide 3: Ladder Hazards
Improper set up
Broken parts
Worn treads
Overload
Improper use
Wrong type
Over-reaching

## Slide 4: Types of ladders
Step Ladder
Extension Ladder
Platform Ladder
Trestle Ladder

## Slide 5: Don’t forget PPE
Fall protection for extended work on ladder.
Footwear with good support and non-slip soles.
Safety Glasses for overhead work.
Other PPE required for specific tasks.

## Slide 6: Work Area Safety Check
No Electrical power lines in area.
Level surface for ladder placement.
Sturdy support for resting ladder top.
Not in a traffic area.
Ladders must not be placed in front of doors that open toward the ladder unless the door is blocked open, locked, or guarded.

## Slide 7: Pre-Use Safety Check
No damage to ladder sides, rungs, supports
Non-slip Feet
Long enough for the job.
Rungs & steps free from slip hazards.
Nonconductive side rails for use where you or ladder could contact exposed energized parts.

## Slide 8: Operation Safety
Face ladder when climbing up or down.
Use tool bag or belt to allow us of both hands when climbing.
Do not carry heavy or bulky items up or down a ladder.
One person on ladder at a time.
Do not over-extend from ladder line.
Secure ladder at bottom.
Fully open step ladders.

## Slide 9: Extension or Single Rail Ladders
Ladders used for access to the roof or to a platform must extend at least 3 feet above the step off point.
A proper ladder angle is achieved by placing the base at a distance from the vertical wall equal to one-fourth the working length of the ladder.

## Slide 10: Ladder smarts
Do not use a ladder in a horizontal position for scaffolding or as a platform.
Ensure base is level and on solid ground.

## Slide 11: Ladder Storage
Vertical Storage – hang from near top rung.
Horizontal storage – provide hooks every 6 feet and near both ends to prevent bowing.

## Slide 12: Ladder Repairs
Repair ladders only with approved parts from the original manufacturer.
Frequently lubricate metal bearings of locks, wheels, pulleys, etc.
Tag broken ladders with a “DO NOT USE” tag.