## Slide 1: Roofing fall protection

## Slide 2: Topics covered
Fall arrest equipment.
Inspection and maintenance of fall protection equipment.
Rescuing a fallen co-worker.
The fall protection work plan.
Notes: “These are the topics that WISHA says we must cover in training our employees who use fall protection.”

## Slide 3: Fall Arrest
Fall Arrest – type used in roofing
  Personal Fall Arrest – full body harness is the most common.

## Slide 4: Fall Arrest Equipment
Personal Fall Arrest:
  A full body harness is a common fall arrest system used in roofing.
  A full body harness stops a fall in progress and minimizes the force of the fall to your body.
  Waist belts not allowed because a fall will usually result in injury.

## Slide 5: Fall Arrest Equipment
Full Body Harness
  The attachment point on a full body harness is a D-ring on your upper back.
  It must be an commercial ANSI Class III harness. Recreational climbing harness are not allowed.
  Be sure to use a size that fits you properly.

## Slide 6: Fall Arrest Equipment
If you fall, the high force of the fall is concentrated at your waist rather than the 6 points of a full body harness.
Why Waist Belts Are Not Safe…
Notes: “ A fall with a waist belt on will usually cause internal injuries. A heavy person will probably tip over and fall head-first out of the waist belt in a fall.”

## Slide 7: Fall Arrest Equipment
Some fall arrest gear comes with a shock-absorbing lanyard.
Must be adjusted to prevent hitting ground or lower level.
In a fall, the equipment stretches several feet.
Notes: “Some lanyards are self-retracting.”

## Slide 8: Anchors
Fall arrest equipment is only as good as the anchor:
  An anchor must be able to withstand 5000 lbs. of force without failing.
  Manufactured anchors must be installed according to manufacturer’s instructions.
  Check pre-installed anchors before using.
  In a fall, your life depends on the anchor holding.
Notes: “ 5000 pounds is the weight of a mid-size pickup truck. When you install an anchor or decide to use an existing one, keep in mind that that anchor must hold the equivalent of a pickup truck. Eyebolts are not recommended since they can pull out too easily under high forces.”

## Slide 9: Anchor Strength
These commercial anchors will support 5000 pounds when installed according to manufacturer’s instructions.
But, what about knots tied to buildings?

## Slide 10: Knots and Anchor Points
A knot can be used to secure a lifeline to an anchor point only when:
  You know the breaking strength of the lifeline.
  The knot does not decrease the strength of the lifeline below 5000 lbs.
Truss peak used as anchor point
Notes: “This kind of anchor can be used on trusses, provide the conditions mentioned are met. This picture shows a double half-hitch or round turn which reduces the strength of the rope by 30-35%.”

## Slide 11: Knots and Anchor Points
Rope-Breaking Strength
Material Diameter | Manila | Polypro | Dacron | Nylon
5/8 in. | 3470 | 4858 | 6940 | 8675
17 mm | 3987 | 5882 | 7974 | 9967
18 mm | 4477 | 6268 | 8954 | 11,192
¾ in. 19 mm | 4997 | 6996 | 9994 | 12,492
Notes: “ This chart shows the breaking strength in pounds of different kinds of life-line rope.”

## Slide 12: Fall Arrest Equipment Use
Knots in ropes or lanyard can reduce strength by as much as 50%.
Protect rope or lanyard from sharp edges.
Notes: “ Knots are not prohibited, but they must not reduce the strength of the rope below 5000 pounds.”

## Slide 13: Fall Arrest Equipment Use
Snap hooks:
  Must be locking type.
  Never hook two snap hooks together.
Notes: “Snap hooks must also have minimum breaking strength of 5000 pounds.”

## Slide 14: Fall Arrest Equipment Use
Some Equipment Do’s and Don’ts:
  Do inspect for wear and damage before use.
  Do remove from service after a fall for inspection.
  Don’t use to lift materials.
  Don’t attach to guardrails or hoists.
Notes: “ Don’t attach to hoist unless you are using the hoist to gain access to the roof.”

## Slide 15: Fall Arrest Equipment Use
Fall Arrest Gear Inspection
Look for the following:
  Webbing - Cuts, tears, abrasion, fraying, stretching, mold, chemical damage.
  D-rings - Cracks, breaks corrosion, rough edges.
  Tongue-buckle - Distortions, added holes, broken grommets.
  Ropes - Abrasion, internal damage.
Notes: [Inspection of employees’ personal fall arrest equipment can be done here.]

## Slide 16: Handling Tools & Materials
Describe here your procedures for handling, storing and securing tools and materials at the jobsite.

## Slide 17: Overhead Protection
Describe how will you protect any employees working or passing through area below roof from overhead items dropping on them such as:
  Hard hats
  Warning signs
  Warning line designating a material
  handling area
  Toe boards on walkways and decks

## Slide 18: Fall Protection Rescue
Describe rescue methods here – self-rescue or assisted rescue using ladders, aerial lifts, forklifts, etc. Also describe first aid measures for injured fallen worker, and how will get medical treatment.
Notes: [Calling 911 in some areas does not ensure prompt rescue since some 911 responders are not equipped or trained to rescue an injured worker suspended from a building.]

## Slide 19: Fall Protection Plan
Fall Protection Plan For Every Job
We are required to prepare a fall protection plan for every job.
Be prepared to go over this plan with your crew boss or lead worker at the beginning of every roofing job.
Notes: [You can show an example of a fall protection plan from previous jobs here.]

## Slide 20
Notes: “New York City in the 1930’s. Is there a net down there somewhere?”